## Slide 1: Spectral and Spectral-element Time Discretizations
Nathan L. Mundis
Department of Mechanical Engineering

## Slide 2: Summary of the Thesis
Introduction (Presented)
The Discretization of the Euler Equations
  Governing Equations (Presented)
  Spatial Discretization
  Temporal Discretizations
    Time-implicit Method (BDF2) (Presented)
    Time-spectral Method (TS) (Presented)
    Quasi-periodic Time-spectral Method (BDFTS)
    Spectral Element Method in Time (SEMT) (Presented)
Structural Equations (Presented)

## Slide 3: Summary of the Thesis
Solution Method
  Fully Implicit Method (Presented)
    Spatial Jacobian
  Linear Solver (Presented)
    Block-colored Gauss-Seidel (BCGS) (Presented)
    Generalized Minimal Residual Method (Presented)
Other Details of Implementation
  Gust Prescription by the Split Velocity Method
  Implementation
Time-spectral Flow Results
  Test Case 1: Pitching Motion in Two Harmonics
    Performance Comparison of Solver Variants
  Test Case 2: AGARD Test Case No. 5
    Convergence Study
    The Effects of Additional Preconditioning

## Slide 4: Summary of the Thesis
Time-spectral Aeroelastic Results
  Aeroelastic Test Case (Presented)
    Error Variation as Convergence Tolerance is Relaxed (Presented)
    Convergence Variation with Freestream Mach Number (Presented)
    Convergence Variation with Reduced Frequency (Presented)
  Other Aeroelastic Results
    Rotary Wing Aeroelastic Response
    Gust Response
BDFTS Flutter Results
SEMT Results
  Validation of the SEMT Discretization
  Full SEMT Solution of the Euler Equations (Presented)
    An ODE with a Second-derivative Discontinuity
  A Continuously Differentiable Airfoil Motion (Presented)
  Summary of the SEMT Results
Conclusions and Future Work (Presented)

## Slide 5: TS Introduction
For time-accurate CFD solutions, the most commonly used time-implicit strategies must be solved sequentially, with each subsequent time step following the previous time step
In other words, an effect always follows its cause
This is analogous to walking any path, always putting one foot in front of the other

## Slide 6: TS Introduction
However, many time-accurate problems of interest to engineers are purely periodic, or strongly periodic, in nature
These include wind-turbine flows, rotorcraft flows, turbomachinery flows, and vortex shedding problems
In the walking analogy, this is like walking in a circle or in a slowly moving circle

## Slide 7: TS Introduction
When a problem is periodic, each instance in time is coupled not only to the past but to the future as well
What happens now happens in exactly the same way one period in time later
Since this is the case, periodic (spectral) functions, i.e. sines and cosines, can be used to describe the progression of the solution in time
THIS is the time-spectral method

## Slide 8: TS Introduction
It turns out that 3 points in time uniquely determine a linear combination of a constant mode and a single harmonic of the spectral basis:
Similarly:
  5 points can describe 2 harmonics
  11 points can describe 5 harmonics
  31 points can describe 15 harmonics
  points can describe harmonics

## Slide 9: TS Advantages
All distinct points in time (time instances) are coupled to all other points in time which allows for a precise solution
All time instances can be solved at the same time (in parallel)
Since all time can be solved simultaneously, the same problem is computationally larger when discretized using the time-spectral method than it would be using traditional time-implicit, thus time-spectral methods can more effectively use larger computing clusters
Since the time-spectral method produces a purely periodic solution, a properly chosen initial guess has less impact on the convergence time than it does for a time-implicit solution

## Slide 10: Airfoil Demonstration

## Slide 11: SEMT Introduction
Like the time-implicit method, time is discretized into multiple time steps (or time elements)
Within each time step, a polynomial is used to describe the variation of the conserved variables
As more elements are added, the error should theoretically decrease as the degree of the polynomial within the element (for sufficiently smooth variation of the variables)
As element degree is increased, the error should decrease exponentially, like time-spectral
In sum, these properties mean that fewer elements should be necessary than when BDF2 is used

## Slide 12: Formulation: Base Solver
Base Solver
  Flow governing equations in Arbitrary-Lagrangian-Eulerian(ALE) form for a General Conservation Law
  Euler equations are discretized by a central difference finite-volume cell-based scheme with additional matrix-based artificial dissipation on hybrid meshes

## Slide 13: Formulation: BDF2
For traditional second order time-implicit (BDF2), the time derivative term is discretized using a second-order backward difference formula:
Where is the solution at the previous time step and is the solution two time steps ago
Substituting this into the Euler equations, we get the following equation for BDF2:

## Slide 14: Formulation: Time-spectral Method
Time Derivative Term
Fourier Transform
Fourier Inverse Transform
for an odd number of N
Time-spectral coupling coefficients

## Slide 15: Formulation: Time-spectral Method
  The discrete equations become:
  The time-spectral method may be implemented without any modifications to an existing spatial discretization, requiring only the addition of the temporal discretization coupling source term

## Slide 16: Formulation: SEMT
Discretize the conserved variables in time element (m) as follows:
where is the kth Lagrange basis polynomial of degree N, as follows:
where and are the locations of quadrature points and with . The transforms from to and back are:

## Slide 17: Formulation: SEMT
The Gauss-Lobatto quadrature points and rule is used. The conserved variables are substituted into the Euler equations and minimized using the
Bubnov-Galerkin method:
where is a weight function. Integrating the above by parts, the following is obtained:
which is then integrated using the Gauss-Lobatto quadrature rule to obtain the equation on the next slide:

## Slide 18: Formulation: SEMT

## Slide 19: Formulation: Backward-only SEMT
Each spectral element in time is treated as an initial value problem with its initial condition given by the end point of the previous element.
The matrix is modified as follows to account for the initial value:

## Slide 20: Formulation: Stability
Stability of the Time-spectral Method
  The time-spectral system of equations can be solved in the common way by adding a pseudo-time term
  For an explicit approach, stability considerations limit this pseudo-time step as:
  This same pseudo-time step is a good approximation to restore diagonal dominance to the Jacobian when such dominance is required for the linear solver in an implicit formulation

## Slide 21: Formulation: Fully-implicit method
Fully-implicit method
  The impact of the pseudo-time step restriction can be mitigated by us of a Newton method which takes the following form:
  With the resultant Jacobian given by:
  The implicit method utilizes a global Newton scheme where a linear system of equations must be solved at each non-linear iteration

## Slide 22: Formulation: GMRES
The resultant linear system can be efficiently solved at each non-linear iteration using the Generalized Minimal Residual Method:

## Slide 23: Formulation: BCGS
Block-colored Gauss-Seidel is used to precondition GMRES in line 4 of the previous algorithm with an additional defect correction step

## Slide 24: Formulation: Details
A pseudo-time step term (as given below) is used for enhanced diagonal dominance, a better-conditioned matrix, and to limit the size of the update:
If the off-diagonal entries are omitted from , this corresponds to a system that is implicit in space but explicit in time

## Slide 25: Formulation: Preferred Solver
Attaining efficiency superior to time-implicit methods hinges on the ability to rapidly solve the large non-linear system resulting from time-spectral discretizations
  Use of a fully-coupled, fully-implicit Newton method with preconditioned GMRES as the linear solver allows such a rapid solution
  Use of GMRES also makes TS methods more robust, especially when applied to problems that require large numbers of time instances to resolve the broad range of harmonic content, such as the ones presented herein
  Use of a defect-correction in the preconditioner allows that preconditioner to be more efficient and effective

## Slide 26: Structural Motion

## Slide 27: Structural Equations
: mass of the airfoil
: static imbalance
: sectional moment of inertia
: plunging spring coefficient
: pitching spring coefficient

## Slide 28: Non-dimensional Structural Equations
The addition of the breve indicates the derivative is taken in structural time , not flow time
Please refer to the thesis for more details.

## Slide 29: First-order Form: Structural Equations
To solve the structural equations, they are transformed into first order form:

## Slide 30: Solution of the Structural Equations
The time derivative term in the structural equations is discretized using BDF2, TS, or SEMT, whichever matches the discretization of the flow equations
For all three time discretizations, the fluid and structural equations are coupled implicitly and solved using FGMRES

## Slide 31: Aeroelastic Results: Test Case
NACA-0012 Airfoil
8747 triangular elements
Freestream Mach:
Prescribed pitching motion
is specified via a reduced frequency
Aeroelastic response in pitch and plunge
The elastic axis is half a chord length in front of the airfoil

## Slide 32: Aeroelastic Test Case: Lift Coefficient Comparison

## Slide 33: Aeroelastic Test Case: Pressure Drag Coefficient Comparison

## Slide 34: Aeroelastic Test Case: Moment Coefficient Comparison

## Slide 35: Aeroelastic Test Case: Error Comparison to BDF2
is considered well converged: 512 time steps and 63 time instances

## Slide 36: Aeroelastic Test Case: Efficiency Comparison to BDF2
Near-exact time-implicit solution: 512 time-steps per period,
9,680 seconds
Near-exact time-spectral solution:
63 time instances,
5,665 seconds

## Slide 37: Aeroelastic Test Case: Efficiency Vs. Cd Error Comparison
Near-exact time-implicit solution: 512 time-steps per period
Near-exact time-spectral solution: 63 time instances

## Slide 38: Aeroelastic Test Case: Efficiency Vs. Cd Error Comparison
Near-exact time-implicit solution: 512 time-steps per period
Near-exact time-spectral solution: 63 time instances

## Slide 39: Summary of Aeroelastic Test Case Results
The time-spectral method with up to time instances converges in less wall-clock time than the time-implicit solution with time steps per period (near exact solution) using one CPU core per time instance
However, if time-spectral is scaled to the same 16 CPU cores as were used for the time-implicit solution, up to only time instances can be run more quickly than the time-implicit solution with time steps per period
The time-implicit, aeroelastic solutions need many more periods to arrive at a purely periodic solution than is the case when aeroelasticity is neglected

## Slide 40: Freestream Mach Number:
Near-exact time-spectral solution:
7 time instances, 276 seconds

## Slide 41: Freestream Mach Number:
Near-exact time-spectral solution:
47 time instances, 2,263 seconds

## Slide 42: Freestream Mach Number:
Near-exact time-spectral solution:
47 time instances, 4,349 seconds

## Slide 43: Efficiency Variation with Freestream Mach Number

## Slide 44: Reduced Frequency: 0407
Near-exact time-spectral solution:
79 time instances, 4,598 seconds

## Slide 45: Reduced Frequency:
Near-exact time-spectral solution requires more than 95 time instances and would take over 6 hours to converge

## Slide 46: Efficiency Variation with Reduced Frequency
?

## Slide 47: BDF2 Error and Efficiency Variation with Convergence Tolerance
9,680
4,980

## Slide 48: TS Error and Efficiency Variation with Convergence Tolerance
1,696
6,678
5,665
22,306

## Slide 49: TS Concluding Remarks
Preconditioned, flexible GMRES with aeroelastic coupling included at all solution levels allows for the efficient and robust solution of time-spectral aeroelastic problems
Exponential error convergence is observed for many of the time-spectral cases
The GMRES-DC solver developed is more than an order of magnitude more efficient than the simplest aeroelastic, time-spectral solver that was attempted near the inception of this work
The time-spectral convergence tolerance can be relaxed to a great degree and the accuracy of the solution still retained

## Slide 50: SEMT Results: Test Case 1
NACA-0012 Airfoil
8747 triangular elements
Freestream Mach:
Prescribed pitching motion
is specified via a reduced frequency (quasi-steady)
The period is

## Slide 51: SEMT Test Case 1 Average CL Error

## Slide 52: SEMT Test Case 1 Instantaneous CL Error

## Slide 53: SEMT Test Case 1 Instantaneous CL Error

## Slide 54: SEMT Results: Test Case 2
NACA-0012 Airfoil
8747 triangular elements
Freestream Mach:
Prescribed pitching motion
is specified via a reduced frequency (quasi-steady)
The period is

## Slide 55: SEMT Test Case 2 Average CL Error
3.80
5.07
5.44

## Slide 56: SEMT Test Case 2 Instantaneous CL Error

## Slide 57: SEMT Test Case 2 Instantaneous CL Error

## Slide 58: SEMT Test Case 2 Instantaneous CL Error

## Slide 59: SEMT Concluding Remarks
The theoretical rate of error h-convergence can be observed over a limited range for sufficiently smooth solutions of the Euler equations
Discontinuities, even in the derivatives of the solution variables, can cause large oscillations within the elements containing them
Mis-specification of the initial condition appears to corrupt the solution (somewhat) at all later times, limiting how precise the solution can be at those later times
Methods exist to address these problems as will be discussed in later, in the Future Work section

## Slide 60: Thesis Summary
Robust, efficient solution of the Euler and aeroelastic equations discretized with TS, BDFTS, and SEMT has been demonstrated for a wide variety of problems of interest
FGMRES has allowed problems with as many as 127 time instances to be solved
For the most efficient solution, coupling of disparate sets of equations should be included at every solution level: non-linear residual, FGMRES, defect correction, and BCGS preconditioner
The current framework is best for problems:
  That are weakly compressible (i.e. )
  That have low reduced frequencies
  That have content in only the first few harmonics

## Slide 61: Advancement to the Field
Increasing the number of time instances that can be used in the time-spectral network
  127 time instances (63 harmonics) solved
  No upper limit in sight
Implicit, aeroelastic time-spectral solution
  This work represents the first application of the time-spectral method to implicitly-coupled aeroelastic problems
Quasi-periodic time-spectral flutter analysis
  This work represents the first application of the BDFTS method to fixed-wing aeroelastic flutter analysis
Application of the SEMT to the Euler equations
  It is believed that this work represents the first application of the SEMT tot eh Euler equations
  Theoretical order of error convergence was demonstrated for 1st through 5th degree elements

## Slide 62: Advancement to the Field
Increasing the number of time instances that can be used in the time-spectral network
  127 time instances (63 harmonics) solved
  No upper limit in sight
Implicit, aeroelastic time-spectral solution
  This work represents the first application of the time-spectral method to implicitly-coupled aeroelastic problems
Quasi-periodic time-spectral flutter analysis
  This work represents the first application of the BDFTS method to fixed-wing aeroelastic flutter analysis
Application of the SEMT to the Euler equations
  It is believed that this work represents the first application of the SEMT tot eh Euler equations
  Theoretical order of error convergence was demonstrated for 1st through 5th degree elements

## Slide 63: Future Work
Solver Efficiency Improvements
  The solver is more than an order of magnitude more efficient than the first time-spectral solver that was used in this work
  An optimal time-spectral solver would allow the wall-clock time to convergence to remain constant for any number of time instances so long as one CPU core is used per time instance
  The current solver uses much more than the optimal amount of time for large numbers of time instances and this trend worsens when freestream Mach number and reduced frequency are increased
  Despite this non-optimality, the TS method can still solve most aeroelastic problems in less wall-clock time than the time-implicit method because of the additional parallelism in time, the increased number of periods needed to obtain a purely periodic solution in the case of the aeroelastic, time-implicit method, and the less strict convergence tolerance that time-spectral methods allows
  Solver efficiency needs to be further improved through the implementation of better preconditioners for FGMRES:
    Linear-agglomerated multigrid
    Incomplete LU factorization
    Combinations of different types

## Slide 64: Future Work
Flutter Frequency Determination for BDFTS Flutter Analysis
  A method must be developed that allows the determination of the actual frequency of flutter with a BDFTS flutter solution is being found
Adjoint based hp-refinement in Time
  For TS, automatic p-refinement would allow a solution of a specified precision to be found with an engineer having to constantly add time instances to see if the solution changes
  For BDFTS, different periods of the solution could have different numbers of time instances so that the precision of the final solution was within a specified threshold, without wasting time instances in periods that do not need them
  For SEMT, hp-refinement could be used to cluster time elements in areas of sharp time gradients and discontinuity while also choosing the best degree to use within each element to minimize error at the lowest computational cost

## Slide 65: Future Work
Artifical Viscosity in Time
  While hp-refinement is one method to address discontinuities, another is the introduction of artificial viscosity in time that would “smear” out these discontinuities so that the solution became computationally smooth
Cell-discontinuous time-spectral method
  In the current time-spectral scheme, all cells in the spatial mesh use the same number of time instances
  A new scheme could be developed where each cell of the spatial grid only had as many time instances as were needed to resolve the objective of the analysis to a given precision
  Different cells would have different numbers of time instances
  p-refinement in time could be used to ensure enough time instances were used in each cell
  A scheme of this nature would likely not be discretely conservative, so analysis must be done to assess the scheme

## Slide 66: Future Work
Monolithic-time and Periodic SEMT
  These two other methods for coupling spectral elements in time have not yet been implemented and should be explored
Deforming Meshes
  All problems in the thesis used rigid mesh motion
  3D problems require deforming meshes
  The mesh deformation equations would need to be implicitly coupled to retain the efficiencies developed herein
Discontinous-Galerkin Method in Time (DGMT)
  SEMT is continuous, allowing discontinuity at the end points of the time elements might allow for a better discretization
Fully-implicit Runge-Kutta (FIRK)
  This is another set of higher-order methods that could be applied in the time dimension and might yield better accuracy and convergence than the methods examined thus far

## Slide 67: Questions