## Slide 1: Adjoint-Based Sensitivity Analysis for Computational Fluid Dynamics
Dimitri J. Mavriplis
Max Castagne Professor
Department of Mechanical Engineering
University of Wyoming
Laramie, WY USA

## Slide 2: Motivation
Computational fluid dynamics analysis capabilities commonplace today
In addition to analysis capability, sensitivity capability is highly desirable
  Design optimization
  Error estimation
  Parameter sensitivity
Sensitivities may be obtained by:
  Perturb input, rerun analysis code (Finite difference)
  Linearizing analysis code (tangent method)
    Good for 1 input, many outputs
  Adjoint method (Pironneau, Jameson, many others…)
    Good for many inputs, one output

## Slide 3: Objective
Demonstrate methodical approach for formulating and implementing discrete adjoint to increasingly complex problems
Progressively more complex simulation sensitivity formulations
  Steady-state aerodynamics (3D)
  Time-dependent aerodynamics (2D)
  Time-dependent coupled aero-elastic (3D)
Focus
  Adjoint formulation
    Hand coded (occasional use of AD)
    Same data structures/solution techniques as analysis
    Verification
  Exact full sensitivities in all cases
  Optimization examples are simply illustrative
Time-dependent
Aeroelastic
Overset meshes
Adaptive meshes

## Slide 4: Adjoint Sensitivity Formulation
Continuous vs. Discrete Adjoint Approaches
  Continuous: Linearize then discretize
  Discrete: Discretize then Linearize
Continuous Approach:
  More flexible adjoint discretizations
  Framework for non-differentiable tasks (limiters)
  Often invoked using flow solution as constraint using Lagrange multipliers
Discrete Approach:
  Reproduces exact sensitivities of code
    Verifiable through finite differences
  Relatively simple implementation (but tedious)
    Chain rule differentiation of analysis code
    Transpose these derivatives
      (transpose and reverse order)
    Includes boundary conditions
    Automation possible (but use judiciously for efficiency reasons)

## Slide 5: Adjoint Sensitivity Formulation
Continuous vs. Discrete Adjoint Approaches
  Continuous: Linearize then discretize
  Discrete: Discretize then Linearize
Continuous Approach:
  More flexible adjoint discretizations
  Framework for non-differentiable tasks (limiters)
  Often invoked using flow solution as constraint using Lagrange multipliers
Discrete Approach:
  Reproduces exact sensitivities of code
    Verifiable through finite differences
  Relatively simple implementation (but tedious)
    Chain rule differentiation of analysis code
    Transpose these derivatives
      (transpose and reverse order)
    Includes boundary conditions
    Automation possible (but use judiciously for efficiency reasons)

## Slide 6: Adjoint Sensitivity Formulation
Continuous vs. Discrete Adjoint Approaches
  Continuous: Linearize then discretize
  Discrete: Discretize then Linearize
Continuous Approach:
  More flexible adjoint discretizations
  Framework for non-differentiable tasks (limiters)
  Often invoked using flow solution as constraint using Lagrange multipliers
Discrete Approach:
  Reproduces exact sensitivities of code
    Verifiable through finite differences
  Relatively simple implementation (but tedious)
    Chain rule differentiation of analysis code
    Transpose these derivatives
      (transpose and reverse order)
    Includes boundary conditions
    Automation possible (but use judiciously for efficiency reasons)

## Slide 7: Discrete Adjoint Formulation (a simplified view)
Objective:
Subject to:
  R = 0 : flow solution converged
  u : flow variables (solution)
  D: design parameters (shape parameters)
Sensitivities:
Constraint sensitivity eqn:
Final form:
easy
hard

## Slide 8: Discrete Adjoint Formulation
Sensitivity equation:
Adjoint equation:
  No dependence on D
  Dependence on L
Final form:
Cost is independent of number of D’s
dL/dD are then used by a gradient based optimizer to find next best shape
Evaluate first, define as LT

## Slide 9: Generalized Discrete Sensitivities
Consider a multi-phase analysis code:
  L = Objective(s)
  D = Design variable(s)
Sensitivity Analysis
  Using chain rule:

## Slide 10: Tangent Model
Special Case:
  1 Design variable D, many objectives L
Precompute all stuff depending on single D
Construct dL/dD elements as:

## Slide 11: Adjoint Model
Special Case:
  1 Objective L, Many Design Variables D
  Would like to precompute all left terms
  Transpose entire equation:

## Slide 12: Adjoint Model
Special Case:
  1 Objective L, Many Design Variables D
  Would like to precompute all left terms
  Transpose entire equation: precompute as:

## Slide 13: Shape Optimization Problem
Multi-phase process:

## Slide 14: Tangent Problem
1: Surface mesh sensitivity:
2: Interior mesh sensitivity:
3: Residual sensitivity:
4: Flow variable sensitivity:
5: Final sensitivity

## Slide 15: Adjoint Problem
1: Objective flow sensitivity:
2: Flow adjoint:
3:Objective sens. wrt mesh:
4: Mesh adjoint:
5: Final sensitivity:

## Slide 16: General Approach
Linearize each subroutine/process individually in analysis code (tangent or forward model)
  Check linearization by finite difference/complex variables
  Transpose to get adjoint, and check duality relation
    Should reproduce same sensitivities to machine precision
Build up larger components
  Check linearization, duality relation
Check entire process for FD/Complex and duality
Use single modular AMG solver for all phases
Maintaining forward linearization has advantages
  Cases with few design variables, many objectives
  Debugging adjoint code
  Enables exact Jacobian/vector products for Krylov solve
    More later…

## Slide 17: Verification: Complex Step
Finite difference approach is plagued by round-off error (small e) versus non-linear error (large e)
  Must find range of e that gives accurate sensitivities
  Sometimes no such range exists
Complex variable approach:
  Replace f(x) with complex function f(x+ie)
  Then df/dx = Im(f(x+ie))/e
  Can take e=1.e-100 (no roundoff error)
  Very accurate gradients (machine precision)

## Slide 18: General Duality Relation
Necessary but not sufficient test
  Check using series of arbitrary input vectors
Analysis Routine:
Tangent Model:
Adjoint Model:
Duality Relation:

## Slide 19: General Duality Relation
Necessary but not sufficient test
  Check using series of arbitrary input vectors
Analysis Routine:
Tangent Model:
Adjoint Model:
Duality Relation:

## Slide 20: Optimization Procedure
Run flow solver to obtain steady solution
Run adjoint solver to compute sensitivities
Compute design variable perturbation as:
Perturb D by dD
Deform airfoil surface as a function of D
Compute objective function Lg
Set dD = 0
start
stop
Check Lg
(or provide gradient to optimizer)

## Slide 21: Drag Minimization Problem
DLR-F6 Wing body configuration (1.2M points)
Mach=0.75, Incidence=1o , Re=3M

## Slide 22: Drag Minimization Problem
Total Optimization Time for 15 Design Cycles:
6 hours on 16 cpus of PC cluster
  Flow Solver: 150 MG cycles
  Flow Adjoint: 50 Defect-Correction cycles
  Mesh Adjoint: 25 MG cycles
  Mesh Motion: 25 MG cycles

## Slide 23: Optimization for Time Dependent Problems
Using chain rule linearization
  New time-step values depend on previous time step values
  Integrate linearized equation in time (tangent problem)
  Transpose all to get adjoint (and reverse order of matrix multiplication)
    Integrate backwards in time
    Requires storing entire time history (to disk)
      10 8-Byte variables per grid point per time step
      Advantage of using large time steps with good implicit solver
      Use local node disks on parallel computer (>1TB each node)
  Similar to data-assimilation problem (4DVAR)

## Slide 24: Time-Integrated Objective Formulation
Pitching airfoil time histories of CL and CD

## Slide 25: Unsteady Flow Solution Mani and Mavriplis AIAA 2007-0060
Pressure Contours for Pitching Airfoils
Minf = 0.755, a0 = 0.016o, amax = 2.51o, w = 0.1628, t=0 to 54
27 time-steps with dt=2.0
NACA0012 Baseline Airfoil
Optimized Airfoil

## Slide 26: Time-Dependent Load Convergence Mani and Mavriplis AIAA 2007-0060

## Slide 27: Dynamic Stall Optimization
Optimized airfoil performance: Objective=Minimize moment excursions at constant lift

## Slide 28: Extension to Multidisciplinary Problems: Time-Dependent Aeroelasticity
Fully coupled problem involves 4 modules:
  Flow solver
  Structural Solver
  Mesh deformation
  Fluid-structure interface (FSI)
Adjoint formulation leads to :
  Disciplinary adjoints: Fluids, Structures, Mesh, FSI
  Disciplinary adjoints are coupled at each time step
  Coupled adjoint solver analogous (transpose) of coupled aeroelastic analysis solver
  Demonstrated flutter suppression through shape optimization in 2D
    Mani and Mavriplis AIAA 2008-6242

## Slide 29: 3D Test Problem
4 bladed Hart-II rotor in hover:
  Rigid blade
  Flexible blade
CFD/CSD specifications:
  2.32 million grid nodes (prisms, pyramids, tets)
  20 beam elements
Tight CFD/CSD coupling
  3 rotor revs (dt=2O)
  6 coupling per time step, 10 CFD and 5 CSD non-linear iterations per coupling
  ~1 hr/rev with 512 cores
CFD flow domain
Rigid and Flexible blades

## Slide 30: Aerodynamic Solver: NSU3D
3D unstructured mesh finite-volume RANS solver
2nd –order accurate in space and time.
One equation Spalart-Allmaras turbulence model.
Deforming mesh capability with GCL compliance
Fully implicit discretization solved using Newton’s method at each time-step as:
  Preconditioned GMRES used for linear system
    Forward linearization used for exact Jacobian-vector products
  Linear agglomeration multigrid for preconditioner
  Line implicit solver as smoother for linear multigrid

## Slide 31
Strong scaling of AMG solver up to 32K cores

## Slide 32: Structural Analysis: Beam Model
Hodges-Dowell type finite element based solver
15 degrees of freedom (flap, lag, axial and torsion)
First order system:
where,
J = Residual of structural equation
q = blade dof (displacements)
F = beam (aero) forcing
Solved via direct inversion
Beam FEM model
Notes: The structural solver is a Hodges-Dowell beam type FEM based solver. Makes use of 15 dof, which includes, flap, lag, axial and torsion dof.
The system of equation is a typical mass-spring-damper type 2nd order system of equations and it can be simplified to a 1st order system of equation, such as:….
The solver has been validated by comparing the predicted fan plot for Hart-2 (Higher harmonic control Aeroacoustic Rotor Test combined program by German/Dutch/French/US in Oct 2001; 40% scaled BO-105) rotor with that from UMARC (UM advanced rotor code). The first three flap modes and 1st torsional mode has been very accurately captured, as shown in the table here for an operating rpm of 381RPM or 6.36hz or 40 rad/s.

## Slide 33: Mesh Deformation
Propagates surface displacements to interior mesh
  Deflections from structural model at each time step (xn)
  Design shape changes (D)
Based on linear elasticity analogy
  (more robust than spring analogy)
Solved using line-implicit agglomeration multigrid (analogous to flow solver)
G(xn,xnsurf,D) = 0
Notes: The structural solver is a Hodges-Dowell beam type FEM based solver. Makes use of 15 dof, which includes, flap, lag, axial and torsion dof.
The system of equation is a typical mass-spring-damper type 2nd order system of equations and it can be simplified to a 1st order system of equation, such as:….
The solver has been validated by comparing the predicted fan plot for Hart-2 (Higher harmonic control Aeroacoustic Rotor Test combined program by German/Dutch/French/US in Oct 2001; 40% scaled BO-105) rotor with that from UMARC (UM advanced rotor code). The first three flap modes and 1st torsional mode has been very accurately captured, as shown in the table here for an operating rpm of 381RPM or 6.36hz or 40 rad/s.

## Slide 34: Fluid-Structure Interface (FSI)
Cloud of surface points associated with beam element
Forces projected onto beam element shape functions
Displacements projected back to CFD surface points using transpose
Notes: The structural solver is a Hodges-Dowell beam type FEM based solver. Makes use of 15 dof, which includes, flap, lag, axial and torsion dof.
The system of equation is a typical mass-spring-damper type 2nd order system of equations and it can be simplified to a 1st order system of equation, such as:….
The solver has been validated by comparing the predicted fan plot for Hart-2 (Higher harmonic control Aeroacoustic Rotor Test combined program by German/Dutch/French/US in Oct 2001; 40% scaled BO-105) rotor with that from UMARC (UM advanced rotor code). The first three flap modes and 1st torsional mode has been very accurately captured, as shown in the table here for an operating rpm of 381RPM or 6.36hz or 40 rad/s.

## Slide 35: CFD/CSD Coupling Time Integration Methodology
Outer loop over physical time steps
  Coupling iterations per time step :
    Mesh:
      Line implicit multigrid
    Flow:
      Implicit BDF2 Newton iterations (GMRES)
      Linear agglomeration multi-grid
    FSI (Fluid to structure)
      Explicit assignment
    Structure:
      Implicit BDF2 newton iteration (direct inversion)
    FSI (Structure to fluid)
      Explicit assignment

## Slide 36: Analysis Convergence
60 non-linear iterations per time step
3 multigrid cycles/iteration
Convergence by 2 orders of magnitude
Rigid blade convergence
Flexible blade convergence
6 coupling cycles per time step
10 non-linear iterations/coupling with 3 multi-grid cycles/iteration
Convergence by 2 orders of magnitude

## Slide 37: Convergence continued…
Mesh convergence per time step
CSD convergence per coupling per time step
Mesh solves upto 60 iterations or 1x10-9 (whichever earlier) per coupling
Mesh convergence by 10 orders of magnitude per time step (6 coupling cycles)
Beam convergence to machine precision (faster convergence)
Notes: Reduction in later coupling mesh sub-iterations for convergence, because coupling is converging by then.

## Slide 38: Blade Tip Time History
Blade tip vs time
Blade flaps to high values, but converges to a lower value after 3 revs
Surface Cp
Blade flap over time
Flexible
Rigid
(m)
Notes: The surface pressure figure shows the existence of shock near the tip of Hart-II rotor blade, predicted both by the rigid as well as the flexible blade analysis. Mtip=0.64, rpm=1041 (109 rad/s)

## Slide 39: Hart-II Performance Prediction
Thrust vs time
Power vs time
Reduced thrust (~2%) and power (~2.5%) predicted by coupled analysis
Notes: Simulating w/o flexible blade would result in overpredicting power penalty.

## Slide 40: Aerodynamic Sensitivity: Tangent
Time-dependent objective function:
Linearizing w.r.t design variable ‘D’:
General expression for forward linearization of objective function w.r.t design variables:
Represents inner product over space and time
Notes: A typical time-dependent objective function looks like: (give examples of L , D etc., define x , D etc.)
Sensitivity of the objective function wrt a design variable (geometric shape parameter) is:

## Slide 41: Aerodynamic Sensitivity: Tangent
Constraint equation to be satisfied: Implicit residual at each time-step.
Linearize w.r.t design variables using chain rule:
System of constraint equations for time step n:
Mesh Motion Solver
Flow Solver
Notes: This is forward linearization or tangent analysis. Equation shows, finding sensitivity vectors require dependence on ‘D’.
Most of the design problems involve multiple ‘D’ and usually a single ‘L’. To overcome dependence of ‘D’ adjoint approach comes to rescue.

## Slide 42: Aero Sensitivity: Tangent
Constraint equation to be satisfied: Implicit residual at each time-step.
Writing in generalized matrix form:
Equations dependent on D
Solution involves integrating forward over entire time domain
Notes: This is forward linearization or tangent analysis. Equation shows, finding sensitivity vectors require dependence on ‘D’.
Most of the design problems involve multiple ‘D’ and usually a single ‘L’. To overcome dependence of ‘D’ adjoint approach comes to rescue.

## Slide 43: Aero Sensitivitiy: Adjoint
Adjoint equations:
Solve adjoint system:
Finally objective sensitivity:
Equations independent of D
Solution involves integrating
backward over entire time domain
Notes: The adjoint approach is a sort of ‘reverse’ process of forward sensitivity formulation, which boils down to solving an system of equations for a pair of adjoint vectors corresponding to ‘mesh’ and ‘flow’, the jacobian being just the transpose of that of the tangent formulation. Sensitivity depends only on ‘L’ and not on ‘D’.

## Slide 44: Structural Sensitivity
Objective function L,
Constraint:
Tangent:
Adjoint:
‘D’ can be structural or geometric shape parameters
Notes: To look at the structural sensitivity, let’s look at a typical time-dependent structural beam objective function (which could be a function of beam deflection co-ordinates).

## Slide 45: Fully Coupled Fluid-Structure Analysis
General solution
Mesh:
Flow:
force transfer:
Structure:
Blade deformation transfer:
Flow and mesh
Force transfer
Structure
Blade deformation transfer
Per coupling cycle
Notes: Fully coupled analysis requires information exchange b/w fluid and structure every time step. This requires 2 additional equations, one for force transfer from CFD to CSD and the other is blade deformation transfer to interior mesh (CSD to CFD).

## Slide 46: Fully Coupled Fluid-Structure Sensitivity: Tangent
Functional sensitivity:
Solve:
Mesh and Flow
Surface force sensitivity
Force transfer and Structure
Deformation transfer
Per coupling
cycle
Notes: x=interior mesh, xs = surface mesh

## Slide 47: Fully Coupled Fluid-Structure Sensitivity: Adjoint
Solve:
Per coupling
cycle

## Slide 48: Coupling Schematic
CFD
CSD
Force (F)
Deformation (XS)
Analysis
CFD
CSD
(dF/dD)
(dXS/dD)
Tangent
CFD
CSD
ɅF
ɅXs
Adjoint
Start
End
Start
End
Start
End
Same data structures
Same solution strategy

## Slide 49: Blade Geometry Parametrization
Hicks-Henne bump functions
Structured blade mesh overlap with CFD mesh
Master blade shape defined by Hicks-Henne bump functions and twist
  Defined by high-resolution structured mesh (in black)
  Shape changes interpolated onto unstructured CFD surface mesh
112 design parameters
  10 Hicks-Henne bump functions per blade section, 11 blade sections (110)
  Twist at blade root and tip (2)
Notes: To test the adjoint sensitivity of a given time-dependent objective function wrt blade geometry shape parameters as design variables, a ‘master blade shape’ is defined by using Hicks-Henne bump functions. The blade shapes are defined across 11 blade sections using 10 bump functions per section. The resulting ‘master blade shape’ is used to define a structured blade surface grid. Finally this surface blade geometry is mapped into the into CFD mesh by interpolating the structured blade surface co-ordinates onto the overlaping CFD surface blade mesh. These bump functions along with rotor twist at blade root and tip allows for 112 design parameters for optimizing blade shape.

## Slide 50: Strongly Coupled Helicopter Blade Optimization
Time-integrated objective function:
Hart-II rotor (2.32x106 grid) run for 2 revs (dt=2o)
Optimizer: L-BFGS-B bounded reduced Hessian
Bounds:
  chord on airfoil section
  o twist
Parallel with 1024 cores
4 design cycles, 5 function calls, 1.4 hours per function call

## Slide 51: Verification of Strongly Coupled CFD/CSD Adjoint Formulation
Time step | Method | 
1 | Complex | 3.690007037237534E-006
 | Tangent | 3.690007037237471E-006
 | Adjoint | 3.690007037237598E-006
2 | Complex | 5.150483530831191E-006
 | Tangent | 5.150483530831145E-006
 | Adjoint | 5.150483530831289E-006
3 | Complex | 5.828069793498591E-006
 | Tangent | 5.828069793498538E-006
 | Adjoint | 5.828069793498741E-006
4 | Complex | 6.056211086344925E-006
 | Tangent | 6.056211086344902E-006
 | Adjoint | 6.056211086345518E-006
5 | Complex | 6.026286742020757E-006
 | Tangent | 6.026286742020644E-006
 | Adjoint | 6.026286742020636E-006
Time step | Method | 
1 | Complex | 3.690007037237534E-006
 | Tangent | 3.690007037237471E-006
 | Adjoint | 3.690007037237598E-006
2 | Complex | 5.150483530831191E-006
 | Tangent | 5.150483530831145E-006
 | Adjoint | 5.150483530831289E-006
3 | Complex | 5.828069793498591E-006
 | Tangent | 5.828069793498538E-006
 | Adjoint | 5.828069793498741E-006
4 | Complex | 6.056211086344925E-006
 | Tangent | 6.056211086344902E-006
 | Adjoint | 6.056211086345518E-006
5 | Complex | 6.026286742020757E-006
 | Tangent | 6.026286742020644E-006
 | Adjoint | 6.026286742020636E-006
Verified to 12 significant digits with complex version of complete coupled analysis
Verified over multiple time steps
Accuracy preserved over multiple time-steps
Notes: Verified to 12 significant digits
Verified over multiple time steps
Accuracy preserved over multiple time-steps

## Slide 52: Blade Optimization Results
Adjoint flow residual convergence by 5 orders
Functional dropping, gradient being reduced
Adjoint flow residual

## Slide 53: Optimized Blade Sections
Thicker inboard and thinner outboard sections
Baseline
Optimized

## Slide 54: Blade Optimization Results continued…
Optimized blade with (6%) less bending
Reduced power (2%) with small thrust (1% reduction)

## Slide 55: Further Work
Optimization examples are illustrative only
More work required
  Objective formulation
  Design variable selection including structural design variables
  Constraints
    Moment constraint (trim)
    Geometrical constraints, flow constraints, Maximum stress constraints , etc
Other areas of research
  Second order methods (hessian matrix)
  Non-local optimization
    Gradient enhanced response surfaces

## Slide 56: Second-Order Methods
Adjoint is efficient approach for calculating first-order sensitivities (first derivatives)
Second-order (Hessian) information can be useful for enhanced capabilities:
  Optimization
    Hessian corresponds to Jacobian of optimization problem (Newton optimization)
      Unsteady optimization seems to be hard to converge
    Optimization for stability derivatives
    Optimization under uncertainty
  Uncertainty quantification
    Method of moments (Mean of inputs = input of means)
    Inexpensive Monte-Carlo (using quadratic extrapolation)

## Slide 57: Forward-Reverse Hessian Construction
Hessian for N inputs is a NxN matrix
Complete Hessian matrix can be computed with:
  One tangent/forward problem for each input
  One adjoint problem
  Inner products involving local second derivatives computed with automatic differentiation
Overall cost is N+1 solves for NxN Hessian matrix
  Lower than double finite-difference: O(N2)
  May be impractical for large number of design variables
  Can get Hessian vector products O(1) cost each

## Slide 58: Hessian Implementation
Implemented for steady and unsteady 2D airfoil problems
Validated against double finite difference for Hicks-Henne bump function design variables

## Slide 59: Newton Optimization with Hessian
LBFGS is “best” gradient-based optimizer
  Constructs approximate Hessian based on previous design iterations
KNITRO is Newton optimizer
  Requires Hessian as input
Superior performance in terms of number of function calls
  Added cost of Hessian recovered (2 to 6 design variables)

## Slide 60: Newton Optimization with Hessian
LBFGS is “best” gradient-based optimizer
  Constructs approximate Hessian based on previous design iterations
KNITRO is Newton optimizer
  Requires Hessian as input
Superior performance in terms of number of function calls
  Added cost of Hessian recovered (2 to 6 design variables)

## Slide 61: Newton Optimization with Hessian
LBFGS is “best” gradient-based optimizer
  Constructs approximate Hessian based on previous design iterations
KNITRO is Newton optimizer
  Requires Hessian as input
Superior performance in terms of number of function calls
  Added cost of Hessian recovered (2 to 6 design variables)

## Slide 62: Extrapolation with Hessian
Computed lift over a range of 1 shape design variable
Linear extrapolation :
Quadratic extrapolation :
Adjoint corrected linear extrapolation equivalent to cost of quadratic

## Slide 63: Aerodynamic Data Modeling

## Slide 64: Aerodynamic Data Modeling

## Slide 65: 2D Airfoil Shape Optimization

## Slide 66: Conclusions
Adjoint formulation is powerful for obtaining sensitivities for problems with large numbers of design variables and few numbers of objectives
Discrete adjoint can be implemented in modular fashion and verified to machine precision
  Using same data-structures/solution strategy as analysis
  Applied to progressively more complex problems
    Steady aerodynamics
    Time dependent aerodynamics
    Time-dependent aero-elastic problems
Beneficial extension possible through
  Hessian formulations
  Non-local optimization using gradient enhanced response surfaces

## Slide 67: Acknowledgements
Faculty
  Jay Sitaraman
Students and Postdoctoral Researchers
  K. Mani, Z. Yang, R. Rumpfkeil, A. Mishra, W. Yamazaki
Alfred Gessow Rotorcraft Center of Excellence at University of Maryland
University of Wyoming ARCC and NCAR-Wyoming Supercomputer Center

## Slide 68
Questions?